##### Item specifics
Place of Origin:	China (Mainland)
is_customized:	Yes
Brand Name:	OEM
Motor Type:	DC Motor
Driver chip:	L298N dual H-bridge driver IC
Storage temperature:	-25 ~ +130
Driver Board Size:	55mm * 60mm * 30mm
Product Description

Feature:
Driver: L298N Dual H Bridge DC Motor Driver IC
Drive Terminal Power Supply: +5 V ~ +35 V; (if others need to be powered by the board, power supply should be +7V~+35V)
Drive Part of the Peak Current: 2A
Logic Terminal Power Supply: +5 V ~ +7 V (Power supply within the board: +5 V)
Logic Part of the Operating Current: 0 ~ 36mA
Control Signal Input Voltage Range: Low:-0.3V Vin 1.5V; High: 2.3V Vin Vss
Enable Signal Input Voltage Range: Low: -0.3 Vin 1.5V (control signal is inactive); High: 2.3V Vin Vss (control signal active)
Maximum Power Consumption: 20W ( at 75 deg C)
Storage Temperature: -25 ~ +130 deg C
Other Extensions: Control indicators, logic unit power supply interface
Size(L x W x H): 55 x 49 x 33mm (includes the height of copper pillar and heat sink)